COEN 6501 Digital design and Synthesis

Oct. 28, 2013                                                   Lecturer: Asim J. Al-Khalili

Answer all Questions. All Questions carry equal marks

Exam Duration: 1hr 30 min.

No books, papers or calculators are allowed.

======================================================

Question 1

Represent the numbers “15.25” and “-0.25” in IEEE 754 floating point format. Add these numbers and show your addition steps. Give an architecture for floating point addition. Question 2

Using 4-bit Ripple Carry Adders and gates implement

F = x2  where x is a 4-bit unsigned number. Show all inputs/outputs and the critical path clearly.

How would you change the design efficiently if X was a signed 2’s complement number.

Question 3

It is required to design an ignition system for a 4-cylinder car. The cylinders C1 to C4, are to fire in sequence of C1-C2-C3-C4-C1-C2-C3 etc. Design a Finite State Machine to produce the outputs for the ignition system. Give circuit diagram and clearly identify the outputs.

# Text boxes

Ignition Circuit

CLOCK

C1

C2

C3

C4